## Slide 1
Vaporization of Liquid Helium and Low Temperature Thermometry
Thomas Collins
Advisor: Professor Karl Slifer
Magnet and Fridge Assembly
Fridge Assembly
Acknowledgements
A huge thank you to all the members of Slifer and Long Lab, Karl Slifer, Elena Long, David Ruth, Nathaly Santiesteban, and Tristian Anderson for all the support
Low Temperature Thermometry Calibration
a = 2.36862708
b = 0.66027805
c = 0.77520692
Thermal Results
The following graphs consist of experimental data collected during the March 2019 cooldown.
Thermal Analysis of the Heating Cartridge
Post Cooldown, a thermal analysis of the heating cartridge was done to observe its effect on the baffle and copper coil tubing. In this analysis the ambient temperature was chosen to be 100K, and the heater power is set to 40W. These characteristics and the thermal coefficients for each part ensured an accurate representation. Figure (i) shows the dissipation from a top down viewpoint and Figure (ii) shows a side profile. Thermal analysis was done using SOLIDWORKS.
Heating Cartridge and Thermometry SOLIDWORKS rendering of the heating cartridge and Allen Bradly thermometry assembly. Located On the second baffle above the separator.
Tempo Doped Araldite Target
Target stick containing the Alpha and Beta target in 3rd and 4th cups. Located on the end of the target ladder on the bottom of the fridge.
Mercury iTC
A Mercury iTC is a cryogenic programmable intelligent temperature controller. This was used to monitor temperature and resistance, while controlling the heating cartridge though a set point temperature or heat flow (%).
Heating Element System
19 Pin Connection
A D9 connector ran from the back of the Mercury iTC to the 19 pin connector. A 19 pin connector was used for electrical connections between the lab space and the vacuum environment.
Heating Element
The heating cartridge and Allen Bradley resistor separated by a copper baffle. Wiring consisted of magnet wire and spade clips connections.
Figure 1 is a graphical visualization of the heater equilibrating to a set point temperature of 100 K.
Figure 2 shows the heater turning off from an set temperature, once 150 sec pass the heater is turned on again. This visualization proves the effectiveness of the heater on the fridge baffles by the corresponding fluctuation between voltage and temperature.
Tempo Doped Araldite Targets
Power Study of Tempo
Tempo Doped Araldite Spin Up

## Slide 2
A set point temperature would use a PID feedback loop to regulate the cryostat temperature. (See Figure i). The heat flow (%) setting would send the heating element with a set % of the max voltage.
The placement on the copper baffle allowed the baffle to act as a secondary heating element through conduction. Its placement within the fridge was determined to directly impact the venting liquid helium while having no effect on the colds pace at the bottom of the helium evaporator.
It carried four leads, two for thermometry and two for the heating cartridge.

## Slide 3
Project Overview
  Our main focus is to develop a rocket propelled by a student designed hybrid engine
      A hybrid rocket engine uses a solid reducer with the assistance of a liquid oxidizer
  Compete in the Spaceport America Cup in June 2020 hosted in Las Cruces, New Mexico
      A 10,000 ft. apogee competition implementing a student researched and developed hybrid class engine
  Design and implement a device to enable the gimbaling of our hybrid rocket engine to control flight dynamics in real time
Department of Mechanical Engineering
Authors: Charlie Nitschelm, Andrew Hosman, Collin Stroshine, Ryan Blatti, Chase Eldridge, Tyler Landry, John Langer, Thomas Collins, Silas Johnson
Advisor: Dr. Todd Gross
Gimbal System
  Preliminary design work was started last year on commercial off the shelf 29mm engines to assist in the application of those techniques on a larger, homemade hybrid engine
HHHHH
Cold Fire Test
  A cold test fire was conducted to examine the oxidizer flow through the injector insert, and to determine the mass flow rate
  Tested the flow regulation system
  Attempted to determine how far we must open the flow regulator in order to get optimal flow through the injector plate
Hot Fire Test
Acknowledgments
A huge thanks to all the members of UNH SEDS, Scott Campbell, Dr. Ivo Nedyalkov, Dr. Alireza Ebadi, Sheldon Parent, Chief Dean, Ronald O’Keefe, TURBOCAM International, Reilly Webb and our advisor Dr. Todd Gross for all the support
Manufacturing
  The combustion chamber and Injector plate were manufactured with the assistance of TURBOCAM International
      Both components made of Aluminum 6061 for ease of manufacturing and Tripoli Experimental Rocket Recommendations
      Injector plate designed so the plate can be reused, but hole inserts can be redesigned and replaced
  The nozzle was manufactured here at UNH by Scott Campbell
Who We Are
  A chapter of the Students for the Exploration and Development of Space, part of a nationwide organization
  A second year engineering organization comprised of students of all classes and CEPS majors
  A primary engineering goal of pursuing the art of high power rocketry with custom-made hybrid engines
  Focused on giving its members a unique experience in the design and manufacturing of rockets and rocket engine components
Oxidizer Tank
A highly pressurized vessel that
contains liquid Nitrous Oxide,
acting as our oxidizer within
the combustion chamber
Flow Regulator
A motorized valve that monitors flow regulation
of the oxidizer into the injection plate controlled
by an electric motor and
an Arduino.
Injection Plate
Responsible for providing desired oxidizer flow into the combustion chamber with the assistance of the impinging plate
Combustion Chamber
An enclosed volume where the solid reducer and liquid oxidizer react to produce a superheated, highly pressurized chamber of gas
Nozzle
Graphite was machined into a de Laval curve responsible for directing the flow of hot gases outside of the combustion chamber into the environment providing thrust
Reducer and Oxidizer
  The fuel selected is Hydroxyl-terminated polybutadiene (HTPB), a commonly used hybrid reducer.
  Liquid Nitrous Oxide was chosen as the oxidizer as it is commonly paired with HTPB and provided us with a great baseline of public knowledge
  A mold was 3-D printed to insert into the combustion chamber and form the rubber to a specific grain formation in preparation for combustion and radial burn rate
Impinging Plate
An interchangeable cylindrical plate responsible for the impingement and atomization of the oxidizer flow streams
Rocket Building Techniques
  To begin designing and manufacturing a rocket engine, it is crucial to understand overall rocket design, mechanics and manufacturing techniques
      Utilized last years members to teach and mentor new members on the lessons learned from last years research
      Hosted multiple building sessions and in-house competitions to compete on highest altitude achieved
  Learned the fundamental parameters that affect the performance of a rocket in flight, and tested first hand the effect of these design choices on the overall flight performance and path.
Two actuators will be utilized to control the pitch and yaw of our thrust vector through flight
An accelerometer will be used to sense any variation in our zenith direction, and quickly redirect our engine thrust to return back to the desired flight path
Project Field Safety
Must obtain a suitable location and testing infrastructure for safe testing procedures and events by communicating and negotiating with local officials
Design certain field structures needed for the development of testing and launching semi-permanent buildings
Engine Startup / Ignition Method
    Correct ignition method to start-up the engine and provide initial heat and pressure for further combustion with the oxidizer
    Obtain an initial injector flow rate
Hot Fire Testing Rig and Data Collection
    Used to safely test the hybrid rocket engine in a static rig
    Collect precise data on thrust, mass flow rate and combustion temperature for future optimization of the hybrid rocket engine geometry