## Slide 1
University of New Hampshire
Students for the Exploration and Development of Space
Journey to Spaceport
A story of UNH SEDS

## Slide 2
University of New Hampshire
Students for the Exploration and Development of Space
The 3-Year Plan
Year One
2017-2018
Rocket Building
Simulating
Launching
Optimizing
Year Two
2018-2019
Hybrid Engine
Engine Design
Manufacture
Test
Runaway
Hybrid Rocket
Spaceport America Cup
Rocket Vehicle
Engine Optimization
Year Three
2019-2020

## Slide 3
University of New Hampshire
Students for the Exploration and Development of Space
Year 1 – Sophomore Year
SEDS Rocketry Competition, May 2018, Maine
Organization Statistics
Committed Members: 11
Majors: 3
Senior Projects: 4
Funding: $2,250

## Slide 4
University of New Hampshire
Students for the Exploration and Development of Space
Year 1 – Rocket Building
Staging Coupler
Supports stage separation at sustainer ignition
Booster Engine
Initiates flight
Drogue Parachute
A small parachute deployed at apogee
Aft Fins
Provides stability to the rocket
Electronics Bay
Houses the TeleMega GPS and controls flight events
Sustainer Engine
Propels the rocket to flight apogee
Booster Parachute
A large parachute for booster landing
Forward Fins
Provides stability to
the sustainer
Sustainer Parachute
The main parachute that slows the sustainer to landing speed
Custom Nose Cone
A 3D printed nose cone that houses the drogue parachute

## Slide 5
University of New Hampshire
Students for the Exploration and Development of Space
Year 1 – Simulating
 | Reported Max Thrust | Measured Max Thrust | Reported Total Impulse | Measured Total Impulse
Booster Engine: H399 | 545.8 N | 549.6 N | 282.2 N-s | 277.1 N-s
Sustainer Engine: I204 | 356.8 N | 329.7 N | 347.7 N-s | 322.7 N-s
Hot Fires of COTS engines to obtain thrust data
Discrete-Event Simulation

## Slide 6
Year 1 – Launching
University of New Hampshire
Students for the Exploration and Development of Space
 | Flight Data | OpenRocket Model | MATLAB Model
Sustainer Apogee | 1071.1 m | 1020.6 m | 1154.1 m
Booster Apogee | 290.0 m | 238.6 m | 276.3 m
Built nine experimental rockets with six being multi-stage
Reduced flight failures from 4 out of the first 5 to 1 out of the last 4.
Rocket 6/9
7% Error

## Slide 7
Year 1 – Optimizing and Repeat
University of New Hampshire
Students for the Exploration and Development of Space
Research Aerodynamic Theory
Improve Field Launch Techniques
Launch and Gather Data
Optimize Rocket Dimensions
Manufacture and Assemble
Improve
Aerodynamic Models
Check Integrity with Finite Element Analysis
Improve Manufacturing Techniques
Rocket Improvement Cycle
Uses our in-house simulations in a nonlinear solver to converge on a set of rocket dimensions
Refined simulations to match experimental data from ± 35% on 1st rocket to ± 5 % on the last

## Slide 8
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Junior Year
Organization Statistics
Committed Members: 20 (+9)
Majors: 5 (+2)
Senior Projects: 9 (+5)
Funding: $5,500 (+$3,250)
Spacevision 2018, November 2018, San Diego

## Slide 9
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Hybrid Engine
Oxidizer Tank
A highly pressurized vessel that contains liquid Nitrous Oxide
Flow Regulator
A motorized valve that monitors flow regulation of the liquid oxidizer
Injection Plate
Responsible for providing desired oxidizer flow into the combustion chamber
Combustion Chamber
An enclosed volume that produces heated, highly pressurized gas
Nozzle
Machined into a de Laval curve responsible for directing the flow of hot, pressurized gases
Impinging Plate
An interchangeable plate responsible for the flow streams of the oxidizer

## Slide 10
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Engine Design
Injector and Impinging Plate
Oxidizer Selection and Flow Regulation
Needs to be self pressurizing
Needs to be safe to handle
Can be refilled within a day
Nitrous Oxide meets these requirements
Suitable for ground testing
Ability to throttle
1000 psi rated valve/tubing
Cheap – 150 dollars
Interface with COTS piping from flow regulator
Quick testing of different impinging geometries
Transitions the liquid oxidizer to a gas
From past hybrid papers: ~400 psi and 700 K

## Slide 11
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Engine Design
Nozzle
Combustion Chamber
Withstand internal operating conditions
Hold a volume of fuel (HTPB) to support the defined mixture ratio (~6)
Seals with the nozzle and injector flanges
Accelerate the hot gases within the combustion chamber using converging/diverging design
Withstand a corrosive, high temperature environment
Designed these components in Solidworks, no experience with NX but understand differences (tree, solid bodies, no convert entities)
From past hybrid papers: ~400 psi and 700 K

## Slide 12
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Manufacture
Combustion chamber chucked on the lathe machined by a machinist at TURBOCAM
Molding the rubber into the combustion chamber
Assembly of the flow regulator
Runaway fully assembled with the aluminum chamber, injector and graphite nozzle
Machining and assembly of impinging plate

## Slide 13
University of New Hampshire
Students for the Exploration and Development of Space
Year 2 – Test
Control bunker for hot-fire tests
Hot-fire test 1 – Ignition
Obtain thrust and temperature data during the hot-fire test
Electric spark and igniter assembly
Rapid impinging plate designs tested for impingement and desired flow rate

## Slide 14
University of New Hampshire
Students for the Exploration and Development of Space
Year 3 – Senior Year
Organization Statistics
Committed Members: 42 (+31)
Majors: 7 (+4)
Senior Projects: 14 (+10)
Funding: $9,000 and counting (+$6,750 so far)

## Slide 15
University of New Hampshire
Students for the Exploration and Development of Space
Year 3 – Rocket Vehicle
Avionics
An electronics module responsible for GPS tracking, engine ignition and flow control
Recovery System
A recovery module that is deployed at apogee
Research Payload
A payload built in-house to collect data
Throttle Control
A flow regulation system to insert oxidizer flow into the chamber
Runaway
New Hampshire’s first hybrid rocket engine that utilizes a liquid oxidizer and solid fuel
Oxidizer Storage
A pressurized vessel holding the liquid oxidizer

## Slide 16
University of New Hampshire
Students for the Exploration and Development of Space
Year 3 – Engine Optimization
Hot-Fire Test 2 – August 2019
.15 seconds in, nozzle brittle failure from tension
Simulations underestimated pressure and designed to FOS 1.25  bad decision
Stainless 304 selected for new nozzle
Provides a FOS of 3
Common material for temperature and corrosive resistance
Machined by a new sponsor
Future Engine Development
Obtain pressure data from hot fires
Pressure testing via hydrostat
Flow simulations to optimize nozzle and impinging plates
Reduce mass with dynamic sims
Hot-Fire Test 4 scheduled for October 31th by 5:00 pm EST
Cleaner electronic start sequence
Stainless nozzle
SPT25-20-1000A
0-1000 psi
12V DC operating voltage
Corrosion and heat resistant (SS sensor)

## Slide 17
University of New Hampshire
Students for the Exploration and Development of Space
Rocket competition hosted in New Mexico from June 16th to June 20th
UNH SEDS will be competing in the 10,000-foot experimental hybrid engine category
Other categories include solid, liquid, and hybrid with 10,000-ft and 30,000-ft

## Slide 18
University of New Hampshire
Students for the Exploration and Development of Space
Questions?